MATERIAL SAFETY DATA SHEET

Product Name: Candle Lacquer 0218 – xxxxx							             Page 1/5

Date of revision: 23. Jan. 2007 Replace: 17. Nov. 2006 Data Sheet no.: 0218 			Version no.: 3 Date of printing: 23-01-2007

Candle Lacquer 0218 – xxxxx						en

1. 	1. IDENTIFICATION OF THE SUBSTANCE/PREPARATION AND COMPANY

Product Name: Candle Lacquer 0218 – xxxxx				PR-no:

Product Category: Acrylic resin-based paint.

Manufacturer:							Emergency telephone number :

Cawatec A/S							The doctor may contact the

Rungstedvej 75							Danish Poisons Information

DK-2960 Rungsted Kyst						Center by calling: +45 35 31 60 60.

Telephone no.:	+45 45 16 16 11

Fax no.: 		+45 45 16 16 12

Uses:

Decorative coating for wax candles.

2.	 COMPOSITION/INFORMATION ON INGREDIENTS:

Hazardous compounds in accordance with EC Directives 1999/45/EEC; 2001/59/EEC (symbol and R-phrases are stated for 	the pure compound). Any volatile compounds are stated in item 8 in units of ppm.

Contains:

CAS number:	EINECS no.:	%:  	Chemical Name:   	Classification: 	Note:

67-64-1		200-662-2		25-50%	acetone		Xi, F		R11, R36, R66, R67

1330-20-7		215-535-7		10-25%	xylene		Xn, Xi		R10, R38, R20/21

100-41-4		202-849-4		2,5-10%	ethylbenzene	Xn, F		R11, R20

64742-48-9	265-150-3		<2,5%	Naphtha (petroleum), 	Xn		R65, R66	4,H

hydrotreated heavy

3. 	HAZARDS IDENTIFICATION:

Main Toxicological and Ecological hazards:

This product is very flammable and presents a hazard to health.  Irritating to eyes.  Irritating to skin.  Harmful by inhalation and in contact with skin.

4. 	FIRST AID MEASURES:

General information:

If in doubt, seek medical advice. Also see para. 1

Inhalation:

If patient feels unwell move to fresh air and keep under surveillance.  If the victim is unconscious, ascertain whether the victim is breathing.  If breathing has stopped, apply artificial respiration.  If the victim is unconscious but breathing, place in the recovery position and keep warm with blankets.  Obtain immediate medical attention or call an ambulance.

Contact with eyes:

If necessary, remove contact lenses. Immediately flush eyes with water for at least 10 minutes. Hold eyelids wide apart. 	Seek medical attention.

Contact with skin:

Remove contaminated clothes immediately, and wash skin thoroughly with soap and water. Skin cleaner may be used.

Do not use organic solvents or thinners.

Ingestion:

Do NOT induce vomiting. If vomiting occurs, hold head low to prevent aspiration of liquid into lungs. Obtain medical

help or ambulance.

Burns:

Flush with plenty of water until pain ceases. Whilst flushing with water, remove all loose clothing from area of burns. If

medical treatment is necessary, continue rinsing until a doctor takes over the treatment.

MATERIAL SAFETY DATA SHEET

Product Name: Candle Lacquer 0218 – xxxxx							             Page 2/5

Date of revision: 23. Jan. 2007 Replace: 17. Nov. 2006 Data Sheet no.: 0218 			Version no.: 3 Date of printing: 23-01-2007

Candle Lacquer 0218 – xxxxx

5. 	FIRE-FIGHTING MEASURES:

Suitable extinguishing media:

Extinguish fire with foam, carbon dioxide, powder, or water vapor.

Extinguishing media that must not be used:

Do not use a water jet, as this spreads the fire.

Special hazards:

Fire will produce a thick black smoke.

Special protective equipment:

Products of combustion are harmful and respiratory protection is required.

General information:

Cool closed containers with water.

6. 	ACCIDENTAL RELEASE MEASURES:

Personal precautions:

Avoid inhalation of vapours.  See protective measures in items 7 and 8.

Environmental precautions:

If lakes, waterways or drains become contaminated, inform the environmental authorities.

Methods for cleaning up:

If spillage occurs, prevent material from entering drains or water courses.  Recover spill with non-flammable, absorbent material, e.g. sand, dirt, or granular substances, and place in a disposable container (see item 13).  Clean preferably with cleansing agents.  Avoid using solvents.

General information:

Remove all ignition sources and ensure sufficient ventilation.

7.	HANDLING AND STORAGE:

Handling:

Vapors may form explosive mixtures with air. Prevent the formation of flammable or explosive mixtures. Minimize vapor concentrations. Do not use this material near naked flames or any other ignition source. Electrical installations must be protected according to regulations. The product may be charged electrostatically. Always use underground wire when transferring from one container to another. Personnel should wear antistatic shoes and clothing. Floors should be conductive. Do not use tools which may produce sparks. Avoid contact with eyes and skin. Avoid inhaling vapors and spray mists. Smoking and the consumption of food and drink are not permitted in work rooms. Personal protective equipment: Refer to section 8. Do not eat, drink, smoke or store tobacco, food or drink in work places or areas where there is a risk of contact with the product.

Storage:

Follow the Danish Emergency Management Agency guidelines for flammable liquids. The product must be kept away from children. Store in a tightly closed container and in accordance with the current regulations in a dry and well-ventilated place away from food. Keep away from ignition sources, oxidizing agents and strong acidic and basic substances. No smoking. No admittance to unauthorized persons. Opened containers must be carefully closed and stored upright to prevent any leakage.

8. 	EXPOSURE CONTROLS/PERSONAL PROTECTION:

Engineering Control Measures:

All work must be planned with a view to limit the breathing of fumes and the exposure to the skin. Ensure adequate

ventilation. If this is not possible, use respiratory protection according to the MAL code number.

Respiratory Protection:

Use compressed air full face mask.

Hand Protection:

Use 4H protection gloves.  Break-through time is 8 hours.  Cotton gloves may be used under and a disposable glove over the 4H glove.  Follow the glove manufacturer’s recommendations on use and replacement.

Eye protection:

Use suitable protective goggles or full face mask for protection against splashes.

Body Protection:

If possible, wear special work clothes. When spraying wear coveralls.

MATERIAL SAFETY DATA SHEET

Product Name: Candle Lacquer 0218 – xxxxx							             Page 3/5

Date of revision: 23. Jan. 2007 Replace: 17. Nov. 2006 Data Sheet no.: 0218 			Version no.: 3 Date of printing: 23-01-2007

Candle Lacquer 0218 – xxxxx

General information:

Prevent employee exposure to substances that may be hazardous to pregnancy or breast feeding.

Occupational Exposure Limits:

The specified exposure limit values are in accordance with the Danish National Working Environment Authority's list of

recommended Exposure Limit Values.

CAS number: 	Chemical Name: 				Occupational Exposure Limits:	Note:

67-64-1		acetone					250 ppm   600 mg/m3

1330-20-7	xylene					25 ppm   109 mg/m			H

100-41-4		ethylbenzene				50 ppm   217 mg/m3		K

64742-48-9	Naphtha (petroleum), hydrotreated heavy	25 ppm   145 mg/m3

9.	 PHYSICAL AND CHEMICAL PROPERTIES:

Form:					Liquid

Flash point:				< 21

Density:					0,91-0,96

Fire class				I – 1

Explosion limits:				0,5-13

Weight % organic solvents:		70

VOC content (grams / liter):		673

10. 	STABILITY AND REACTIVITY:

Conditions to avoid:

Stable at normal temperature. When exposed to high temperatures, toxic decomposition products may be formed.

Substances to avoid:

To prevent heat-generating reactions, keep the product away from oxidizing agents and strong acidic and basic substances.

11. 	TOXICOLOGICAL INFORMATION:

Inhalation:

Inhalation of vapors may cause symptoms of poisoning, such as memory and concentration difficulties, abnormal tiredness, irritability. And, in extreme cases, unconsciousness. Prolonged and repeated inhalation of high concentrations may cause damage to liver, kidneys, brain and nervous system.

Contact with skin:

Organic solvents have a degreasing effect on the skin. Repeated and/or prolonged contact with this product may cause

inflammation and irritation. Organic solvents may be absorbed through skin.

Contact with eyes:

Eye irritation. Splashes in the eye may cause irritation.

Ingestion:

Chemical pneumonia may occur if organic solvents enter the lungs through vomiting.  Accidental swallowing may cause vomiting and stomach pains.

12.	ECOLOGICAL INFORMATION:

Ecotoxicity:

Do not dispose of this product in drains, watercourses, or on the ground.

13.	DISPOSAL CONSIDERATIONS:

Disposal considerations:

Waste receptacles must be labeled with black text on yellow background: ”Contains a substance that is affected by the Danish work environmental legislation, on account of a risk of cancer.”  Product residues are classified as chemical waste.

Waste code: 	08 01 11		waste paint and varnish containing organic solvents or other dangerous substances

MATERIAL SAFETY DATA SHEET

Product Name: Candle Lacquer 0218 – xxxxx							             Page 4/5

Date of revision: 23. Jan. 2007 Replace: 17. Nov. 2006 Data Sheet no.: 0218 			Version no.: 3 Date of printing: 23-01-2007

Candle Lacquer 0218 – xxxxx

14. 	TRANSPORT INFORMATION:

ADR/RID:	UN no.			1263

Class:			3

Packaging group:		II

Hazard Identification:	33

Proper Shipping Name:	PAINT

IMDG:		UN no.			1263

Class:			3

Packaging group:		II

EmS:			F-E, S-E

Proper Shipping Name:	PAINT

IATA:		UN no.			1263

Class:			3

Packaging group:		II

Proper Shipping Name:	PAINT

15.	REGULATORY INFORMATION:

General information:

In accordance with the EC Directives 1999/45/EEC; 2001/59/EEC Statutory Order on classification, packaging, labelling, sale 	and storage of chemical substances and products the product is marked as follows:

Contains:		xylene

acetone

Labelling:

F	R11	Highly flammable.

R36	Irritating to eyes.

R38	Irritating to skin.

R66	Repeated exposure may cause skin dryness or cracking.

R67	Vapours may cause drowsiness and dizziness.

R20/21	Harmful by inhalation and in contact with skin.

Highly flammable	S16	Keep away from sources of ignition – No smoking.

Xn		S26	In case of contact with eyes, rinse immediately with plenty of water and seek medical advice.

S29	Do not empty into drains.

S33	Take precautionary measures against static discharges.

S7/9	Keep container tightly closed and in a well-ventilated place.

S36/37	Wear suitable protective clothing and gloves.

Harmful

Special labelling:	Only self-contained breathing apparatus may be used, since the product contains volatile liquids, the vapors of which are not detained by carbon filters.

Uses and Restrictions:

Not to be handled by individuals under the age of 18 years, according to Danish Ministry of Employment's ministerial

order No. 516 of 14th June 1996, concerning young people in employment.

16.	OTHER INFORMATION:

R phrases:

R10			Flammable.

R11			Highly flammable.

R20			Harmful by inhalation.

R36 			Irritating to eyes.

R38			Irritating to skin.

R65			Harmful: may cause lung damage if swallowed.

R66			Repeated exposure may cause skin dryness or cracking.

R67			Vapours may cause drowsiness and dizziness.

R20/21			Harmful by inhalation and in contact with skin.

MATERIAL SAFETY DATA SHEET

Product Name: Candle Lacquer 0218 – xxxxx							             Page 5/5

Date of revision: 23. Jan. 2007 Replace: 17. Nov. 2006 Data Sheet no.: 0218 			Version no.: 3 Date of printing: 23-01-2007

Candle Lacquer 0218 – xxxxx

General information:

The information in this Material Safety Data Sheet is based upon our knowledge and on European Union and national

legislation. The user's working conditions are outside our control. It is the responsibility of the users to fulfill the

requirements set by National Legislation. The information is no guarantee of the properties of the product.

Training advice:

The instructions in this Material Safety Data Sheet are given on the assumption that the product is used as stated in item 1. Restrictions of use and special training requirements must also be complied with. The information in this Material Safety Data Sheet should be regarded as a description of the safety issues concerning the product. Due to a ethylbenzene agent content, this product is affected by Danish National Working Environment Authority's instruction on cancer risk preventive measures when handling substances and products.

Final remarks:

The Material Safety Data Sheet may only be reproduced with the permission of the manufacturer.

References:

EC Directives 1999/45/EEC;  2001/59/EEC Statutory Order on classification, packaging, labelling, sale and storage of chemical substances and products. Classification Order (Ministry of the Environment Statutory  Order no. 559 of 04/07/2002). The List of Dangerous Substances (Ministry of the Environment Statutory Order no. 923 of 28/09/2005).

Corrections:

Technical Data Sheet has been changed.

Drawn up by: GK

Updated by: hb