APPLICATION

for

TREND LACQUER

Before Use:

Stir the lacquer thoroughly as follows:

Stir the metallic pigments, which are heavier than the lacquer and therefore tend to sink to the bottom. Use a flat wooden stir.

Stir for approximately 3 minutes or until the surface of the lacquer gets a metallic shine.

During Use:

The lacquer should be stirred approximately every 5 to 10 minutes.

Viscosity:

The lacquer is delivered ready for use. During the production the lacquer may thicken due to evaporation. The viscosity should therefore be measured continuously and be adjusted to 10 seconds measured with a FORD CUP no. 4.

After Use:

The drum must be closed carefully and stored with a tight-fitted lid in dry conditions at room temperature (approx. 20oC).

2004.01.01